## Slide 1
Processing type | Software / Package |  | 
Targeted | TASQ |  | 
 | MZmine 3 |  | 
Untargeted | Metaboscape |  | 
 | XCMS |  | 
 | Mzmine 3 |  | 
 | MS-DIAL 4.9 |  | 
Notes: ##-AccessibilityAssistant: Skip layout check-##

## Slide 8
XCMS parameters | description
ppm | fluctuation of m/z value (ppm) from scan to scan - depends on the mass spectrometer accuracy
peakwidth | range of chromatographic peak width (second)
mzdiff | minimum difference of m/z for peaks with overlapping retention time (coeluting peak) - must be negative to allow overlap
prefilter (k, I) | a peak must be present in k scans with an intensity greater than I
snthresh | signal/noise ratio threshold
noise | each centroid must be greater than the “noise” value

## Slide 9
XCMS parameters | description
binSize | Size of m/z slices (bins). Range of m/z to be included in a group. Depends on mass spectrometer accuracy.
bw | Standart deviation of the gaussian metapeak that group peaks together.
minFraction | To be valid, a group must be found in at least minFraction*n samples, with n=number of samples for each class of samples. A minFraction=0.5 corresponds to 50%.
max | Maximum number of groups detected in a single m/z slices.

## Slide 10
XCMS parameters | description
smooth method | Regression model to model time deviation among samples (linear or loess).
span | Degree of smoothing of the loess model.
extraPeaks | Number of “extra” peaks used to define reference peaks (or well-behaved peaks) for modeling time deviation. Number of Peaks > number of samples.
minFraction | Minimum proportion of samples with reference peaks. If blank samples are used, minFraction < (1 - proportion of blanks).